## Slide 1: LEARNER GUIDE
1. Plan and prepare for work
© Copyright Easy Guides Australia
Edition 5: Version 1 - March 2019
Introduction to Excavator
General Information
2. Identify and control hazards
5. Shut down and store equipment
3. Check and monitor equipment
4. Operate/use equipment
6. Maintain equipment
9. Relocate equipment
7. Housekeeping
8. Record keeping
10. Attachments
RIIMPO320F

## Slide 2: Introduction to Excavator
Home
Next
Previous

## Slide 3: An example of an excavator
INTRODUCTION TO EXCAVATOR
Home
Next
Previous
Bucket cylinder
Boom cylinder
Cab
Counter weight
Carrier roller
Drive sprocket
Track
Boom
Dipper arm cylinder
Dipper arm (power arm)
Bucket
Link
Rod
Quick hitch
Track roller
Idler wheel

## Slide 4
GENERAL INFORMATION
Earthmoving hazards and risks
The most common hazards and risks with earthmoving work are:
Falls from plant or machinery | Traffic and other mobile plant | Overhead or underground power
Underground gas lines | Water and sewage piping | Rollovers
PC 1.3
31

## Slide 5
GENERAL INFORMATION
Earthmoving hazards and risks (continued)
Noise | Dust | Manual handling
Contaminated soil | Falling into trenches or excavations | UV rays (radiation) from working in the sun
PC 1.3
32

## Slide 6: Decibel levels of common sounds
You must wear hearing protection when operating earthmoving equipment.
This is important because 8 hours of noise at 85 db (decibels), or noise levels of 140 db even briefly can permanently damage
your hearing.
Hearing loss is:
slow
painless
irreversible.
Here are some examples of levels of noise in different environments.
A forest has about 20 db of noise
In an office there might be around 60 db
Standing outside a truck generates about 80 db
A jackhammer generates around 100 db
A jet taking off generates about 120 db
PC 1.3 GENERAL INFORMATION
33

## Slide 7: Chemicals and solvents
Chemicals should always be labelled so that you can easily tell what chemical you are working with. Chemicals should be stored in a safe place where someone cannot accidentally come into contact with them.
Always check the safety data sheet (SDS) before handling any chemicals.
The SDS must be provided to, and understood by, a person using chemicals in the workplace. The SDS will tell you how to safely handle the chemicals.
If you are not sure, put the chemicals in a safe, isolated area and talk to your supervisor.
PC 1.3 GENERAL INFORMATION
34

## Slide 8: Fatigue
Fatigue is an acute, ongoing state of tiredness that leads to mental or physical exhaustion and prevents people from functioning normally. It is more than feeling tired and drowsy, it is a physical condition that can occur when a person’s physical or mental limits are reached.
Fatigue can happen because of work or lifestyle related factors. Fatigue is a significant hazard and can
lead to poor concentration, slow reaction times and increased mistakes.
Work related factors | Lifestyle related factors
Working time Scheduling and planning (for example: rosters, length and timing of shifts) Inadequate rest breaks Lengthy periods of time being awake Insufficient recovery time between shifts Payment incentives that may lead to working longer shifts Environmental conditions (for example: climate, light, noise) Type of work being undertaken (for example: physically or mentally demanding) Work demands placed on the person (for example: time frames, deadlines) The organisation’s culture The person’s role within the organisation. | Inadequate or poor quality of sleep due to sleep disorders Social life Family responsibilities Other employment Travel time Health and wellbeing (for example: nutrition and diet, exercise, pain, illness).
PC 1.3 GENERAL INFORMATION
35

## Slide 9
GENERAL INFORMATION
Dizziness
Confusion
Low motivation
Fatigue (continued)
Signs of fatigue
You should be able to identify signs of fatigue in yourself and others. A person who is affected by fatigue may display the following signs:
Headaches and/or dizziness
Wandering or disconnected thoughts, daydreaming, lack of concentration
Blurred vision or difficulty keeping eyes open
Constant yawning, a drowsy relaxed feeling or falling asleep at work
Moodiness, such as irritability
Short term memory problems
Low motivation
Hallucinations
Impaired decision-making and judgment
Slowed reflexes and responses
Reduced immune system function
Increased errors
Extended sleep during days off work
Falling asleep for less than a second to a few seconds, and being unaware they have done so (otherwise known as micro-sleeps)
Drifting in and out of traffic lanes or missing gear changes and turn offs
when driving.
Managing fatigue
Sleep is the only effective long term strategy to prevent and manage fatigue. While tired muscles can recover with rest, the brain can only recover with sleep. The most beneficial sleep is a good night’s sleep taken in a single continuous period.
PC 1.3
36

## Slide 10
GENERAL INFORMATION
Tools and equipment
Here are some typical tools and equipment you might need.
Personal protective equipment (PPE)
Steel cap boots
High visibility safety vest
Hearing protection
Hard hat
Goggles/glasses
Gloves
Dust mask
Sunscreen
Hand tools
Shovel and levels
Socket sets
Screwdrivers or wrenches
Wire brush
Spanners
PC 1.4, 1.6
46

## Slide 11: Defective parts
If you notice a defective part, for example, a fuse is blown or not working, you should arrange to have it replaced immediately. You must check the rules for your site and your state or territory. In some states only licenced mechanics are allowed to do any repairs.
PC 2.2 GENERAL INFORMATION
48

## Slide 12
GENERAL INFORMATION
Calculations (continued)
Loading a truck to capacity
This truck has an 8 tonne load capacity. Dry beach sand weighs 2 tonnes per cubic metre.
How many buckets will it take to fill the truck to capacity using a bucket with
these dimensions?
Bucket dimensions:
Length = 1 metre
Width = 2 metres • Height = 1 metre
Step 2:
The weight of dry sand is known (see Table of Common Weights).
Dry sand weighs 2 tonnes per cubic metre
Weight of material
= 2 tonnes (per cubic metre)
Step 3:
The bucket has a capacity of 1 cubic metre. So a full bucket of dry sand will weigh 2 tonnes.
Bucket capacity
× Weight of material (per cubic metre)
1 × 2 = 2 tonnes
Each full bucket of dry beach sand weighs 2 tonnes.
Step 4:
Truck load capacity is 8 tonnes.
8 tonnes (truck)
÷ 2 tonnes (per bucket)
= 4 buckets
Step 1:
To calculate the capacity of the bucket, use the formula:
L × W × H ÷ 2 1 × 2 × 1 ÷ 2
= 1 cubic metre
Capacity of the bucket
= 1 cubic metre
Answer:
It will take 4 buckets of sand to fill the truck to capacity.
PC 1.2, 3.1
55

## Slide 13
Plan and prepare for work
Chapter 1
57

## Slide 14: Work Health & Safety Legislative Requirements
‘Laws to keep your workplace safe’
Health and Safety requirements are outlined in Acts, Regulations, Codes of Practice and Australian Standards.
Health and Safety Acts
‘Health and Safety Acts’ are laws that explain how to improve health and safety in the workplace. For example: Model National WHS Act. Occupational Health and Safety Act.
Note: Check which Act is relevant in your State/Territory.
Regulations
‘Regulations’ explain specific parts of the Act.
For example: Part 4.3 – Confined spaces, Part 4.4 – Falls.
Codes of Practice/Compliance Codes
‘Codes of Practice’ are practical guidelines on how to comply with (meet the rules of) legislation. For example: HAZARDOUS MANUAL TASKS Code of Practice.
Australian Standards
‘Australian Standards’ are work guidelines that set the minimum accepted
performance or quality for a specific hazard, process or product.
For example: AS 2550 – Cranes, hoists and winches – safe use set.
PC 1.1 PLAN AND PREPARE FOR WORK
58

## Slide 15
PLAN AND PREPARE FOR WORK
QUESTION 1
What are the National Work Health (WHS) and Occupational Health and Safety (OHS) Acts about?
The Acts explain how to keep your workplace safe and healthy. They explain what you need to do to meet your duty of care.
For example:
You must make sure you do earthmoving work in a way that won’t put yourself or others at risk. You must use earthmoving equipment according to instructions.
Note:
Check your state requirements as Acts may vary from state to state
You must work in a way that is safe. You must not risk the health and safety of yourself or others.
QUESTION 2
Under WHS/OHS laws, what are your responsibilities while working?
PC 1.1
60

## Slide 16
PLAN AND PREPARE FOR WORK
Codes of practice are practical guidelines on how to comply or follow the rules in legislation/laws.
For example:
A traffic management Code of Practice will tell you all the rules a traffic controller must follow. For example, a traffic controller must have a zero percent blood/alcohol concentration/reading while performing traffic control duties.
Australian standards are work guidelines that set the minimum accepted performance or quality for a specific hazard process or product.
For example:
AS2550.1
Powerline distances
This standard tells you the distances you can safely work near powerlines on poles and towers.
QUESTION 3
What do codes of practice explain?
QUESTION 4
What do Australian Standards explain?
PC 1.1
61

## Slide 17
QUESTION 5 What are some examples of documentation you should read before doing earthmoving work? | Health and Safety Acts and Regulations Codes of practice Standards, for example AS 2958 Earthmoving machinery Manufacturers specifications Operators manuals Site requirements and procedures Work or quality requirements Drawings and sketches of the work to be done Company policies and procedures for Employment and workplace relations, Equal opportunity and disability.
QUESTION 6 Why should you check the operator’s manual before using earthmoving equipment? | The operator’s manual tells you how to operate your machine. The manual also tells you about maintenance (how to keep your machine working well).
PLAN AND PREPARE FOR WORK
PC 1.1
62

## Slide 18
QUESTION 7 | Plans – Drawings and sketches outlining what you need to do
What kinds of information | Specifications – rules and details about the job
do you need before | Operational details – how you will do the job
starting work? | Quality requirements of the job – the standards you are expected to meet.
PLAN AND PREPARE FOR WORK
PC 1.2
63

## Slide 19
QUESTION 8 What are quality requirements? | The quality requirements tell you the standards you must meet when doing earthmoving work. They tell you what you need to do and how to do it to satisfy the customer. You may need to follow codes of practice, regulations, national standards etc. | 
PLAN AND PREPARE FOR WORK
PC 1.2
64

## Slide 20
PLAN AND PREPARE FOR WORK
Work instructions explain:
Where the job is
What the job is
How to do the job from start to finish
How to do the job safely
How long the job will take
What to do in unexpected situations like bad weather
What tools and equipment you need
QUESTION 9
What do the job’s work instructions explain?
PC 1.2
65