## Slide 1: Bridge and gantry Crane SAFETY AND LICENCE GUIDE
Produced by:
Training support material for:
TLILIC0006
Licence to operate a bridge and gantry crane

## Slide 2: Parts of a bridge crane
INTRODUCTION TO BRIDGE AND GANTRY CRANE
Resistor banks
Crab
End stop
Beam bridge
SWL
Hoist block
Drivers cabin
Rails
Control panel
Bogeys
2

## Slide 3: What is a gantry crane?
INTRODUCTION TO BRIDGE AND GANTRY CRANE
3
A gantry crane has a bridge beam
which is supported by legs
The legs are mounted on carriages which move along supporting surfaces or deck levels
They have a crab with at least one hoisting mechanism which moves from side to side across the bridge
Gantry cranes are used in factories and outdoor areas including railway and shipping yards

## Slide 4
Conduct routine checks
Chapter 2

## Slide 5
CONDUCT ROUTINE CHECKS
QUESTION 35 | Before you start working. If a hazard arises after you have started work, stop immediately and put controls in place.
When do you put your | 
hazard (risk) controls in | 
place? | 
PC 1.5, 2.2

## Slide 6
CONDUCT ROUTINE CHECKS
QUESTION 36 What type of tagline do you use when you work near powerlines? | Non-conductive rope
QUESTION 37 What is the smallest tagline you can use? | 16 mm 16 mm
PC 3.5

## Slide 7
CONDUCT ROUTINE CHECKS
Warning signs and barriers | Flag person | Traffic controls such as witches hats
Flashing yellow hazard lights to warn people | Scaffolding or a gantry to protect people walking by | Pedestrian/vehicle exclusion zones.
QUESTION 38
How do you control the movement of vehicles, mobile plant or people on site?
PC 1.6

## Slide 8
CONDUCT ROUTINE CHECKS
QUESTION 39 What do you need when working in the dark? | You need enough light to work safely. If the work area is dark, you need extra lighting.
QUESTION 40 | Make sure the crane is parked correctly.
How do you safely access the crane’s cabin? | Use three (3) points of contact. For example, two hands and one foot or two feet and one hand.
PC 2.9, 2.3

## Slide 9
CONDUCT ROUTINE CHECKS
• stretched pin
QUESTION 41 What are some examples of obvious defects on a crane? | Cracks in the structure or welds. Bends or twists (or both) in the structure. Visible rust – especially from welds or joints. Paint flaking. Bolts that are loose. | 
QUESTION 42 | Chips or cracks | Can’t read the working load limit
What sort of damage would |  | (WLL) marking
mean that shackles are |  | 
not safe to use for lifting? |  | 
 | Pin defects – | Bends or twists
 | wrong pin | 
 | pin is missing | 
 | pin won’t screw in. | 
PC 2.4

## Slide 10
CONDUCT ROUTINE CHECKS
Damaged eyes, terminal
attachments or end fittings
Damage from heat the sun or chemicals
Any visible damage at all
Stitching is damaged
The label/tag is missing,
damaged or you can’t read it
Nylon sling has contacted acid or alkaline
Polyester sling has contacted paint, coal tar or paint stripper
Wear and tear or abrasions (rub marks)
on the outside
Damaged sleeve
QUESTION 62
Name some problems that make a synthetic sling unsafe to use.
PC 2.4, 2.5
Wear and tear or burns on the inside

## Slide 11
CONDUCT ROUTINE CHECKS
High strands
More than 10% wear
Stretching
Ferrule is damaged
Core is collapsed
Abrasions
Knots in the rope
Heat damage
Damage to eyes
Thimble is damaged
The SWL or WLL is unreadable
Bends or cracks
More broken wires than are allowed
Loose and springy wires
caused by rust or corrosion
Splice is damaged
Strands are squashed or stuck
Loose strands
(bird-caging)
QUESTION 63
Name some problems that stop you from using a flexible steel wire rope (FSWR) for lifting.
PC 2.4, 2.5

## Slide 12
CONDUCT ROUTINE CHECKS
QUESTION 64
Name some problems that stop you from using a lifting chain for lifting.
The label/tag is missing, damaged or you
can’t read it
Gouge marks or cuts
Cracks or spot welds
Link has more than 10% wear in the diameter
Pitting and or rust
Locked or stretched chain links
Twisted, kinked or knotted
Heat damage
PC 2.4, 2.5

## Slide 13: Test the movements
Test the crane’s movements to make sure everything works and the crane can do all of its movements to full capacity.
The movements you test are:
Long travel
Test the long travel control and move the crane along the rail. Go all the way to both end stops.
Cross travel (crabbing)
Test the cross travel control and move the crab along
the runway. Go all the way to both end stops.
Hoist
Lower and raise the hoist block. This will also test the hoist limit switch.
Grab rotation
Some cranes have an extra movement that lets the grab assembly turn 360 degrees.
PC 2.7 CONDUCT ROUTINE CHECKS

## Slide 14
Transfer loads
Chapter 3

## Slide 15
TRANSFER LOADS
You use the hoist block for raising and lowering the hook.
The block might have one or more sheaves.
Position the hoist block over the load’s centre of gravity.
Position the hoist block
When the hoist block is set up properly it reduces the risk of
load swing, damaging the crane, or overloading the crane.
If required, a dogger can help you set up and position the hoist block.
Centre of gravity
PC 3.2