## Slide 1: LEARNER GUIDE
1. Plan and prepare for work
© Copyright Easy Guides Australia
Edition 6: Version 1 - January 2019
Introduction to Skid Steer Loader
General Information
2. Identify and control hazards
5. Shut down and store equipment
3. Check and monitor equipment
4. Operate/use equipment
6. Maintain equipment
9. Relocate equipment
7. Housekeeping
8. Record keeping
10. Attachments
RIIMPO318F Conduct civil construction skid steer loader operations

## Slide 2: Introduction to Skid Steer Loader
Home
Next
Previous

## Slide 3: An example of a skid steer loader
INTRODUCTION TO SKID STEER LOADER
Operator cab (ROPS and FOPS)
Uprights
Lift arm
Tilt cylinder
Grab handles
Steering lever
Operator seat
Bucket steps
Bucket
Rear lights
Rear door
Track roller
Lift cylinder
Home
Next
Previous

## Slide 4
Plan and prepare for work
Chapter 1

## Slide 5
PLAN AND PREPARE FOR WORK
Who has duty of care?
You have a duty of care. So does anyone who has something to do with the worksite.
Duty of care applies to:
Employers/persons conducting a business or undertaking (PCBU). This includes managers, manufacturers/suppliers, importers, designers, inspectors, etc.
Workers. This includes employees, contractors and sub-contractors, employees of labour hire companies, outworkers, volunteers, etc.
PC 1.1

## Slide 6
PLAN AND PREPARE FOR WORK
Codes of practice are practical guidelines on how to comply or follow the rules in legislation/laws.
For example:
A traffic management Code of Practice will tell you all the rules a traffic controller must follow. For example, a traffic controller must have a zero percent blood/ alcohol concentration/reading while performing traffic control duties.
Australian standards are work guidelines that set the minimum accepted performance or quality for a specific hazard process or product.
For example:
AS2550.1
Powerline distances
This standard tells you the distances you can safely work near powerlines on poles and towers.
QUESTION 1
What do codes of practice explain?
QUESTION 2
What do Australian Standards explain?
PC 1.1

## Slide 7
QUESTION 3 What are some examples of documentation you should read before doing earthmoving work? | Health and Safety Acts and Regulations Codes of practice Manufacturers specifications Operators manuals Site requirements and procedures Work or quality requirements Drawings and sketches of the work to be done Company policies and procedures for Employment and workplace relations, Equal opportunity and disability Standards, for example AS2958 Earthmoving machinery.
QUESTION 4 | The operator’s manual tells you how to operate your machine.
Why should you check the operator’s manual | The manual also tells you about maintenance (how to keep your machine working well).
before using earthmoving | 
equipment? | 
PLAN AND PREPARE FOR WORK
PC 1.1, 1.2

## Slide 8
PLAN AND PREPARE FOR WORK
Step 2:
Convert the layer thickness from millimeters to metres.
To do this divide the layer thickness by 1000
150 mm ÷ 1000 = 0.15 m
Step 3:
Multiply the square metres by the layer thickness to get the cubic metres.
80 square metres × 0.15 m
= 12 cubic metres
This can also be written as: 12 m3 or 12 cubic metres
Step 1:
To work out the square metres, multiply the Length (L) by the Width (W).
L × W = Square metres
4 m × 20 m = 80 square metres
This can also be written as: 80 m2 or 80 square metres
Calculations
Working out how much material you need
The work plan has an area which is 4 metres × 20 metres that must be covered by a layer of road base of 150 mm depth.
How many square metres of road base are to be laid? How many cubic metres of road base will you need?
Answer:
There are 80 square metres of road base to be laid.
You will need 12 cubic metres to cover the area to 150 mm depth.
PC 1.2

## Slide 9
PLAN AND PREPARE FOR WORK
Calculations (continued)
Capacity = L × W × H
2
Length
Height
Width
Cubic capacity of cube
= L × W × H
Length
Height Width
Cubic capacity of bucket
= L × W × H ÷ 2
Cubic capacity is ÷ 2 because of the shape of the bucket (a triangular prism)
How to find the cubic capacity of a bucket
The planner must know the capacity of the loader bucket to be able to plan the job. For example, a machine with a larger bucket will move more material than a smaller bucket in the same number of loads.
PC 1.2, 3.1

## Slide 10
PLAN AND PREPARE FOR WORK
Calculations (continued)
Loading a truck to capacity
This truck has an 8 tonne load capacity. Dry beach sand weighs 2 tonnes per cubic metre.
How many buckets will it take to fill the truck to capacity
using a bucket with these dimensions?
Bucket dimensions:
Length = 1 metre • Width = 2 metres
Height = 1 metre
Step 2:
The weight of dry sand is known (see Table of Common Weights).
Dry sand weighs 2 tonnes per cubic metre
Weight of material
= 2 tonnes (per cubic metre)
Step 3:
The bucket has a capacity of 1 cubic metre. So a full bucket of dry sand will weigh 2 tonnes.
Bucket capacity
× Weight of material (per cubic metre)
1 × 2 = 2 tonnes
Each full bucket of dry beach sand weighs 2 tonnes.
Step 4:
Truck load capacity is 8 tonnes.
8 tonnes (truck)
÷ 2 tonnes (per bucket)
= 4 buckets
Step 1:
To calculate the capacity of the bucket, use the formula:
L × W × H ÷ 2 1 × 2 × 1 ÷ 2
= 1 cubic metre
Capacity of the bucket
= 1 cubic metre
Answer:
It will take 4 buckets of sand to fill the truck to capacity.
PC 1.2, 3.1

## Slide 11
PLAN AND PREPARE FOR WORK
QUESTION 5 What are quality requirements? | The quality requirements tell you the standards you must meet when doing earthmoving work. They tell you what you need to do and how to do it to satisfy the customer. You may need to follow Codes of Practice, regulations, national standards etc. | 
PC 1.2, 1.1

## Slide 12
PLAN AND PREPARE FOR WORK
Plans – Drawings and sketches detailing what you need to do
Specifications – rules and details about the job
Operational details – how you will do the job
Quality requirements of the job – the standards you are expected to meet.
QUESTION 6
What kinds of information do you need before starting work?
PC 1.2

## Slide 13
PLAN AND PREPARE FOR WORK
Work instructions explain:
QUESTION 7
What do the job’s work instructions explain?
PC 1.2
What the job is
How long the job will take
What to do in unexpected situations like bad weather
How to do the job safely
What tools and equipment you need
How to do the job from start to finish
Where the job is

## Slide 14
PLAN AND PREPARE FOR WORK
Examples of the approximate weight of different materials:
1 cubic metre of water = 1 metric tonne
1 cubic metre of earth = 1.9 metric tonnes
1 cubic metre of clay = 1.9 metric tonnes
1 cubic metre of dry river sand = 2.0 metric tonnes
1 cubic metre of concrete = 2.4 metric tonnes
1 cubic metre of coal ash = 0.8 (8/10) of a metric tonne
25 bags of cement (40 kg each) = 1 metric tonne
1000 common bricks = 4 metric tonnes
1 cubic metre of steel = 7.3 metric tonnes
1 cubic metre of copper = 9 metric tonnes
1 cubic metre of lead = 11.4 metric tonnes
Table of weight of common materials
1000 kilograms = 1 tonne
PC 3.1

## Slide 15
PLAN AND PREPARE FOR WORK
QUESTION 8
How can you find out the maximum safe working load (SWL) of the
skid steer loader?
Check the load chart | Check the data plate
Read the markings on the skid steer loader itself | Read the operator’s manual
PC 3.1

## Slide 16
PLAN AND PREPARE FOR WORK
QUESTION 9
How can you find out the weight of a load?
1000 kg
You can find the weight by:
Checking the weighbridge note, consignment note, or other information | Reading the weight marked on the load
Estimate the weight of the load. For example: 1 cubic metre of concrete = 2.4t | Check the load scales fitted to the machine
PC 3.1

## Slide 17
QUESTION 10 How much does a cubic metre of wet sand usually weigh? | Around 1.5 tonnes.
QUESTION 11 How can you find out the specifications and limits of the machine you will use? Specifications include: Load capacity Bucket height, volume and width Lift height Dump clearance. | Read the operator’s manual to find out the limits.
PLAN AND PREPARE FOR WORK
PC 3.1, 1.6