## Slide 1: SLEWING MOBILE CRANE (100T) SAFETY AND LICENCE GUIDE
Training support material for:
TLILIC0014
Licence to operate a slewing mobile crane
(up to 60 tonnes)
Produced by:

## Slide 2: Introduction to Slewing Mobile Crane (up to 100 tonnes)

## Slide 3: What is a slewing mobile crane
INTRODUCTION TO SLEWING MOBILE CRANE (up to 100 tonnes)
This learner resource does not cover front-end loader, backhoe, excavator or similar equipment when configured
(arranged or set up) for crane operations.
Rough terrain slewing crane
A slewing mobile crane is a powered crane which features a boom or jib that can slew from front to back. The crane is mounted on a vehicle.
Slewing mobile crane Crawler crane

## Slide 4: Parts of a slewing mobile crane
INTRODUCTION TO SLEWING MOBILE CRANE (up to 100 tonnes)
Running rope
Counter weight
Pigstyed packing
Boom or jib
Head sheave
Hook
Hook block
Rear outrigger
Front outrigger
Outrigger beam
Jack
Hoist rope
Winch
Operators cabin
Drivers cabin

## Slide 5: Element 1 – Plan work / task

## Slide 6: Outriggers and packing
Outriggers (which can also be called stabilisers) are beams or legs that extend out from a crane, helping to keep it stable. Packing is placed under the outriggers to distribute the weight of the crane and load. Outriggers should always be used in accordance with the manufacturers instructions.
Some important things to remember when setting up and packing outriggers are:
Outriggers should be fully extended (if possible). If not the crane may become unstable during lifting. NOTE: Outriggers can be partly extended if allowed by the manufacturer’s specifications and instructions. | Make sure the ground is firm and can bear the load
Packing must cover as much area as possible to distribute load | The packing should be made of hardwood and free from any defects.
PC 1.2 ELEMENT 1 — PLAN WORK/TASK

## Slide 7
ELEMENT 1 — PLAN WORK/TASK
CHAPTER 1 – PLAN WORK/TASK
Hazard versus risk
What is the difference?
Different hazards and risks emerge constantly—sometimes instantly.
Hazard
A hazard is any thing or any situation which could injure or harm you.
In other words, it is anything that can hurt you.
Risk
A risk is the chance of a hazard causing harm such as injury, illness or even death.
In other words, how likely it is that somebody or something may be harmed by the hazard.
PC 2.1

## Slide 8
ELEMENT 1 — PLAN WORK/TASK
Personal Protective Equipment (PPE)
PPE is clothing or equipment worn on the body to protect you from hazards.
PPE will not take away the risk of harm altogether, but it will help
keep you safe.
Safety gloves
Insulated
Long pants
Long sleeved shirt
Safety shoes
Rubber soled, fully enclosed foot, may be steel capped to protect the toes
Safety helmet
or hard hat
Ear muffs or ear plugs
Respiratory equipment
Dust mask, half face respirator or full face respirator
Safety glasses or goggles
High visibility clothing
Safety vest, hi-vis shirt or hi-vis jumpsuit
Safety harness
Lanyard
PC 1.5, 2.2

## Slide 9
ELEMENT 1 — PLAN WORK/TASK
Zones/areas to check for hazards:
Identifying workplace hazards
Workplace hazards need to be identified before you start work.
Take a good look at your workplace and decide if anything could possibly cause injury to you or anyone else in the area.
Ground to eye level
You should check around eye height for:
other equipment
machinery/plant
people
pedestrians
things in the path of travel
insufficient lighting
weather conditions
dangerous materials
surrounding structures
facilities
other obstructions.
Above eye level
You should check above eye level for:
powerlines
other overhead services
buildings
trees
surrounding structures and facilities
other obstructions
bridges.
Ground level (and below)
You should check the ground to see if:
the surface is stable and level
there is debris or rubbish in the way
the surface is strong enough to support the weight of any equipment or materials
if there are any open trenches or recently
filled trenches/excavations
unstable ground
underground services
suspended slabs.
PC 1.5

## Slide 10
ELEMENT 1 — PLAN WORK/TASK
QUESTION 33
A crane is moving a load on a windy day.
What hazards can the wind cause?
The crane could slew out of control
The load could spin
The load could swing
The crane could become unstable
The crane could be damaged
Wind pressure on the load
10
PC 1.5

## Slide 11
ELEMENT 1 — PLAN WORK/TASK
QUESTION 43
What hazard controls can you use for vehicles or plant on the job?
Some methods you can use are:
Flashing yellow hazard lights to warn people
Warning signs
A flag person to control the traffic
Vehicle exclusion zone
Barricades (safety fences)
11
PC 1.6

## Slide 12
ELEMENT 1 — PLAN WORK/TASK
QUESTION 44
How can you warn and control people on site?
Some methods you can use are:
A flag person to control the traffic
Warning signs
Barricades (safety fences)
to protect people
Flashing yellow hazard lights to warn people
Hoardings (Scaffolding or a gantry)
Pedestrian / vehicle exclusion zone
12
PC 1.6

## Slide 13: Element 2 – Prepare for work / task
13

## Slide 14: Too dark
Control
Use extra lighting such as portable lamps, or try to find a
brighter area if you can.
Hazard
If the work area is dark or dimly lit you might not be able to see clearly.
You must be able to see clearly. Ask your boss to have the area properly lit up. They may need to set up temporary lighting while you work.
14
PC 2.2 ELEMENT 2 – PREPARE FOR WORK/TASK

## Slide 15: Flash/bang rule
After you see lightning count the seconds until you hear thunder
Every 3 seconds means the lightning is 1 kilometre away
For example, a 30 second gap means the lightning is about 10 kilometres away
You should NOT work if lightning is within a 15 kilometre radius
If a storm is approaching you should cease work until safe to do so.
The flash/bang rule is an indication only and you should find out what your workplace rules are.
PC 2.10 ELEMENT 2 – PREPARE FOR WORK/TASK
15

## Slide 16: Element 3 – Perform work / task
16

## Slide 17
ELEMENT 3 – PERFORM WORK/TASK
Configuration The configuration of the crane includes things like: The outrigger set up (if applicable) The length and angle of the main boom Operating radius Maximum line load and winch capacity Fly jib and hook attachments. | Important information Other important information may include: Limitations of boom angles Operational conditions. For example wind speed. | Crane set-up A load chart refers to a crane that is set up: According to manufacturers specifications On firm, level ground In ideal weather conditions With outriggers/stabilisers fully extended (where applicable) Tyres correctly inflated and in good condition. Read all of the information on the load chart.
Load chart
All cranes have their own load chart. They should be in place and readable. The load chart gives information about the load
capacity of the crane in a given configuration (set up). The cranes capacity changes depending on how the crane is set up.
Introduction to load charts
PC 3.1
17

## Slide 18: How to read a load chart
18
To calculate the maximum load you can safely lift, there are some basic rules for all load charts. Look at the following
Load chart X, which is for a 20 tonne hydraulic crane.
Follow the steps:
Outriggers
Choose the outrigger set up. This will help you know which section of the load chart to look at. For this example, look at the Without outriggers on the chart. The crane is set up to mobile on rubber.
Boom length
Choose the length of the boom. This will help you know which column to look at. In this example, we’ll use a boom length of 14.06 metres.
Operating radius
Choose the operating radius. This will help you know which row to look at. For this example we’ll use 4.30 metres.
Round up to 4.50 metres.
Capacity
Read down the boom length column and across the operating radius row. This is the capacity (WLL) of the crane. In this example it is 5200 kg.
Hook block/s
The weight of the hook block/s is part of the load. Deduct the weight from the capacity. These weights are on the load chart. In this example, deduct 200 kg for a 3 sheave
hook block.
Jib weight
The weight of the jib (fly), either fitted or stowed, is part of
the load and may be a deduction from the capacity.
This information is on the load chart. In this example, we can’t use the jib because we are not using outriggers.
Line (hoist rope)
Look at the hoist rope reeving to work out how many parts of line (hoist rope) you need to support the load. In this example, the load being lifted is 5 tonnes. The hoist rope has a capacity of 3340 kg which is less than 5 tonnes so you need 2 lines to safely lift the load.
Jib configuration
Find the information about the load capacity of the different jib configurations. This information is in the Jib load
ratings-kgs on the bottom right-hand side of the chart. With jib offset the crane has more capacity, but the jib is meant to give you more lifting height. Some load charts will have information on auxiliary jibs and their limitations.
PC 3.1 ELEMENT 3 – PERFORM WORK/TASK

## Slide 19: READING LOAD CHARTS For Cranes Up to 100 Tonnes
ELEMENT 3 – PERFORM WORK/TASK
Load Chart -
Minimum
Boom Angle
Maximum Jib load ratings in kilograms (KGs)
Jib Length in metres (M)
9
KGs
21
Radius
(M)
10 Offset
Radius
(M)
80.00 7.6
75.00 11.1
70.00 14.0
65.00 17.4
60.00 20.2
55.00 23.5
12
Radius
KGs (M)
8,700 8.4
7,800 11.9
7,100 14.8
4,600 18.2
3,400 21.0
2,500 24.3
15
Radius
KGs (M)
7,395 9.8
6,630 12.9
6,035 16.2
3,910 19.6
2,890 22.4
2,125 25.7
18
Radius
KGs (M)
4,437 10.9
3,978 13.0
3,621 17.3
2,346 20.7
1,734 23.5
1,275 26.8
2,884 12.0
2,586 15.5
2,354 18.4
1,525 21.8
1,127 24.6
1,020 27.9
KGs
2,019
1,810
1,648
1,067
1,014
918
20 Offset
80.00 8.8
75.00 12.3
70.00 15.2
65.00 18.6
60.00 21.4
55.00 24.7
8,200 9.6
7,300 13.1
6,600 16.0
4,100 19.4
2,900 22.2
2,000 25.5
6,970 11.0
6,205 14.5
5,610 17.4
3,485 20.8
2,465 23.6
1,700 26.9
4,182 12.1
3,723 14.0
3,366 18.5
2,091 21.9
1,479 24.7
1,020 28.0
2,718 13.2
2,420 16.7
2,188 19.6
1,359 23.0
1,183 25.8
918 29.1
2,175
1,936
1,750
1,087
947
734
30 Offset
2,382
2,104
1,887
1,114
3,403 14.8
3,006 18.3
2,696 21.2
1,591 24.6
1,061
80.00 10.0
75.00 13.5
70.00 16.4
65.00 19.8
60.00 22.6
55.00 25.9
7,700 10.8
6,800 14.3
6,100 17.2
3,600 20.6
2,400 23.4
1,500 26.7
6,545 12.6
5,780 16.1
5,185 19.0
3,060 22.4
2,040 25.2
1,275 30.7
5,236 13.7
4,624 17.2
4,148 20.1
2,448 23.5
1,632 28.2
1,020
Hook block weight - (KGs)
Single Line Weighted Hook
1 Sheave Hook Block
3 Sheave Hook block
5 Sheave Hook Block
200 kg
360 kg
450 kg
500 kg
Maximum Jib Load Ratings
Deductions
Deductions apply when lifting from beam
point with jib erected use ratings for
36 metre boom and apply appropriate
deductions for lengths less than 36 metres
use boom angle to determine load rating
in 36 metre column for angles not shown
using rating of next Tower boom angle.
NOTE:
Please read the ‘Reading Load Charts for all crane classes’
before reading this section.
19

## Slide 20
Configuration The configuration of the crane includes things like: The outrigger set up (if applicable) The length and angle of the main boom Operating radius Maximum line load and winch capacity Fly jib and hook attachments. | Important information Other important information may include: Limitations of boom angles Operational conditions. For example wind speed. | Crane set-up A load chart refers to a crane that is set up: According to manufacturers specifications On firm, level ground In ideal weather conditions With outriggers/stabilisers fully extended (where applicable) Tyres correctly inflated and in good condition. Read all of the information on the load chart.
Load chart
All cranes have their own load chart. They should be in place and readable. The load chart gives information about the load
capacity of the crane in a given configuration (set up). The cranes capacity changes depending on how the crane is set up.
Introduction to load charts

## Slide 21
ELEMENT 3 – PERFORM WORK/TASK
Element 3 – Perform work / task

## Slide 22
ELEMENT 3 – PERFORM WORK/TASK
Do the lift
This part of the book is about how to do a lift.
It covers:
Positioning the hoist block and boom/jib
Test lifts
Moving and watching the load
Safe crane operation
Responding to unsafe situations
Checking the planned route.
22
PC 3.2, 3.3

## Slide 23
ELEMENT 3 – PERFORM WORK/TASK
The crane is working properly
To make sure:
QUESTION 119
Why is it important to do a test lift?
The load is secure
The load is stable
The crane is stable
23
PC 3.4

## Slide 24
Element 4 –
Pack up
24

## Slide 25
ELEMENT 4 – PACK UP
Leaving the crane unattended
If you leave the crane overnight you should:
Secure (lock) the crane
Raise the hook to a safe height
Retract the boom
Turn off the crane power (if possible).
Remove the load
Shut the crane down according to the manufacturer’s instructions.
Restrict access to the crane.
Unattended loads
Do not leave a load hanging from the crane hook after shutdown or when the crane is left unattended.
The load may lower, swing or become unstable..
PC 4.5
25